ME326 - INTERMEDIATE FLUID MECHANICS

EXAM 1

NAME: __________________________________

STUDENT NUMBER: _____________________

SOLVE BOTH PROBLEMS

| PROBLEM | MARK |
| --- | --- |
| 1 |  |
| 2 |  |
| TOTAL |  |

Problem 1 (50 points)

For a boundary layer over a flat plate assume that

Use the von Karman momentum integral to determine

a)  Boundary layer thickness.

b)  Momentum thickness.

c)  Local skin friction coefficient Cf.

d)  Drag coefficient CD.

Problem 2 (50 points)

A viscous fluid is between two concentric				 ω2

cylinders of radii a and b, which are rotating

respectively, at constant angular velocities of ω1

and ω2 in the counterclockwise direction as

shown.  Assume an axisymmetric, steady flow 						a     ω2

for which there is no axial velocity.

a) Write down the differential equations of						  b

motion in its simplest form.

b) Specify the boundary conditions.

c) When b = 2a and ω1 = ω2 = ω, obtain the

velocity profile as a function of r, ω and a.

d) Given that pressure at r = a is Po, determine

the pressure as a function of r, ω and a.

Navier-Stokes Equation

Cartesian

Cylindrical

Continuity

Convective Time Derivative

Laplacian operator

The r-momentum Equation

The θ-momentum Equation

The z-momentum Equation

Boundary Layer

,		,	   ,

,